## Slide 1: GRAY CODE
Digital Logic Design
Prepared for FY Engineering Students

## Slide 2: WHAT IS GRAY CODE?
Gray code is a binary numbering system where two successive values differ in only one bit.
It is also called Reflected Binary Code.

## Slide 3: WHY GRAY CODE?
✔ Reduces errors
✔ Avoids glitches
✔ Used in encoders
✔ Used in Karnaugh maps

## Slide 4: NORMAL BINARY VS GRAY CODE
Binary Sequence:
000
001
010
011
100
101
110
111
Gray Code Sequence:
000
001
011
010
110
111
101
100

## Slide 5: RULE TO CONVERT BINARY TO GRAY
Step 1: Copy MSB
Step 2: XOR current bit with previous bit

## Slide 6: EXAMPLE
Binary: 1011
Gray:
1
1⊕0 = 1
0⊕1 = 1
1⊕1 = 0
Gray Code = 1110

## Slide 7: RULE TO CONVERT GRAY TO BINARY
Step 1: Copy MSB
Step 2: XOR result with next gray bit

## Slide 8: APPLICATIONS
✔ Shaft encoders
✔ ADC
✔ Karnaugh map
✔ Communication

## Slide 9: ADVANTAGES
✔ Minimizes error
✔ Only 1-bit change
✔ More reliable

## Slide 10: DISADVANTAGES
✘ Complex conversion
✘ Not suitable for arithmetic

## Slide 11: MCQ
Binary: 1101
Find Gray code
A) 1011
B) 1001
C) 1110
D) 0101

## Slide 12: THANK YOU
Questions?